## Slide 2: Project structure and general timeline
Participants in WP2:

## Slide 3: WP2 :: Objectives
WP2: „Interconnection Optimisation and Power Plant System Services“
Objectives:
  to develop a design tool and procedure for the optimisation of the electrical design of offshore wind farm clusters…
  ….including the provision of power plant system services by the cluster.

## Slide 4: WP2 :: Models :: DTU :: CorWind
CorWind model of DTU has the ability to:
  quantify the wind power variability by simulating correlated wind speeds over a large geographical area, i.e. North Sea;
  for large number of wind farms and with time steps down to one second;
  the output can be wind speed and/or power (individual wind turbines, wind farm level or group of wind farms);
  it uses as input climate data and simulates the stochastic variability inside the hour.
Climate model resolution

## Slide 5: WP2 :: Models :: SINTEF :: NET-OP
Tool to find optimal offshore grid expansions
Example – North Sea offshore grid:
Allowed new connections
Existing connections
Optimal new connections
(capacity indicated)
Energy Research
Notes: These figures show an example of previous use of the NET-OP tool to find optimal offshore DC grid expansion.
- The left figure shows the starting point, with existing grid and allowed expansions (that are included in the optimisation). Each country is represented by one node, with generation and load.
- The right figure shows the result of a simulation (under certain assumptions). Chosen grid expansions are indicated in green, with capacities as sown. Nodes are coloured according to whether they have both load and generation (pink), only load, only generation (blue) or no load or generation (black).

## Slide 6: WP2 :: Models :: CIEMAT :: Integrated models
Autoregressive Models
Fuzzy Logic
Neural Nets
etc.
Final Prediction and Confidence Band
Advanced Integration
Wind Farm Output
Advanced
MOS
Power Curve Modelling
Microscale Modelling:
Orography, Roughness, Obstacles
Wind Farm Output
On-line
Data
Statistical Model
Exogenous Variables
Statistical
Dynamical
Mesoscale: WRF
PBL
modelling
GCM
LAM
Integration between Dynamical Model (NWP based approach) and
Statistical Model (Time Series based approach)
by CIEMAT/Global Forecasters
Wind Power Prediction
Expertise on Short- and Very Short-term Prediction

## Slide 7: WP2 :: Models :: IWES :: WCMS
Wind Cluster Management System.
Grid calculations, weather forecast processing, set points for wind farms.
Applications: frequency control, active and reactive power control, reserve provision.
Into EERA-DTOC scope:
    State-of-the-art electrical models for cluster operation in WP2;
    Re-development required  Become into a simulation tool.
Cluster control
Control
strategy
Control
strategy
Control
strategy
Control
strategy
Forecast
engine
WF
Driver
TSO
WCMS Engine
WF Sim
v 1.0.0
WF Sim
Driver
Driver manager
DB
Dispatch
Scheduler
Forecast
engine
Dispatch
WCMS Engine
DB

## Slide 8: WP2 :: Academic and Industrial Partners
  Identification of offshore wind power plant design and control to provide conventional plant services.
  Grid codes compliance.
  Grid connection and cabling interconnection design.
  Know-how transfer regarding grid connection from offshore platforms to onshore electrical grid.
  Grid connection dimensioning for Hexicon wind farms (5+ platforms).

## Slide 9: WP2 :: Models :: Interactions
CorWind model
NET-OP model
Grid optimization
Steady-state
WCMS model
Analysis of the availability of power plant system services
Off-shore development
Wake modelling
Analysis on variability & predictability
P,Q
P,Q
P,Q
P,Q
P,Q
Grid Codes compliance
PSS/e & PSCAD/EMTDC
Transient analysis
2.4
2.3
2.2
2.1
WP1
Fraunhofer IWES
SINTEF
Fraunhofer IWES
Strath
Statoil
Hexicon
Risoe DTU
Fraunhofer IWES
CIEMAT
Strath
SINTEF

## Slide 10: WP2 :: Deliverables
2.1. Power output variability and predictability
M2.1: Tool Module
D2.8
Design tool module
Report on design tool
18
Risoe DTU
Fraunhofer
CIEMAT
2.2. Grid connection and cabling interconnection design
D2.1
D2.2
D2.3
Design tool module
Design procedure
Report
12
SINTEF
Fraunhofer
Starth
Statoil
Hexicon
2.3. Design verification and grid code compliance
D2.4
D2.5
12
Verification procedure x2
Strath
SINTEF
2.4. Analysis of the availability of power plant system services of a cluster
D2.6
D2.7
15
18
Simulation tool
Analysis (report)
Fraunhofer

## Slide 11: WP2 :: Timeline
WP
2.4
WP
2.3.2
WP
2.3.1
WP
2.3
WP
2.2.2
WP
2.2.1
WP
2.2
WP
2.1.2
WP
2.1.1
WP
2.1
CIEMAT‘s
model
WCMS
model
WF designs & test scenarios
CorWind
model
Test scenarios & input data (correlations)
NET-OP
model
Module
Module & Procedure for grid design (PSS/e)
Procedure for Verification GC Compliance
Test scenarios & input data (correlations)
Grid design (PSS/e)